## Slide 1
Nathan Loretan
August 2017, Trondheim Norway
Professor HES-SO: Medard Rieder
Professor NTNU: Dag Roar Hjelme
Contact at Nordic: Torstein Heggebo
Analyse of Zephyr’s Performances
Bachelor’s Thesis
Notes: Exchange students, Switzerland
Collaboration with HES-SO & Nordic, help from NTNU
Not technical presentation
Not vs, more compare
Me, no idea about Nordics components, Zephyr, SoftDevice, ...

## Slide 2
Conclusion
Results
Measurements
Software
Hardware
Specifications
Table of Contents
Table of contents
Introduction
Specifications
Hardware
Software
Measurements
Results
Conclusion

## Slide 3
Conclusion
Results
Measurements
Software
Hardware
Specifications
Introduction
What Nordic provides
Customers use
  SoftDevice → API for Bluetooth Low Energy
  Nordic SDK → API for GPIO, Serial Communication, …
  If necessary
  RTOS, e.g. FreeRTOS
But
  Versions of SoftDevice and Nordic SDK not adaptable with every SoC
  If required, RTOS in addition of SD and SDK
  SoC with memory requirement to use complex RTOS
Why could Zephyr RTOS be another solution ?

## Slide 4
Conclusion
Results
Measurements
Software
Hardware
Specifications
Introduction
Why Zephyr RTOS ?
Open source RTOS designed for IoT application
Easily Portable
Supports multiple hardware architectures
Licensed Apache 2.0
Maintained on public GitHub Repository
Zephyr Project = SD + SDK + RTOS
Notes: Apache 2.0:
- all copies, modified or unmodified, are accompanied by a copy of the licence
- all modifications are clearly marked as being the work of the modifier

## Slide 5
Conclusion
Results
Measurements
Software
Hardware
Specifications
Introduction
However
Important to know
  the performance of Zephyr
  the behaviour of Zephyr with high BLE traffic
Contribution
  Fix a bug nRF5x SPI driver configuration
Added for my project
  nRF52840 GPIO Port 1 Driver
  nRF52840 SPI2 Driver

## Slide 6
Conclusion
Results
Measurements
Software
Hardware
Specifications
Goals
Measure the performance of Zephyr RTOS
  Power Consumption
  Interrupt Latency
  Bluetooth Low Energy Behaviour
Compare with Bare Metal system using Nordic SD+SDK
Important: not determine which one is the best
To do this
  Create Application Peripheral and central
  Use cases
  Test cases
Notes: - Measure important elements for embedded system
Not the Best, SD+SDK as Reference
Application,
  Peripherals, acquire data and central, receive data
  P&C because maintain connection
  real condition
  acquire data from sensors
  Stress the systems
Use cases for application, commnication with BLE
Test cases element enabled with

## Slide 7
Conclusion
Results
Measurements
Software
Hardware
Specifications
Peripheral

## Slide 8
Conclusion
Results
Measurements
Software
Hardware
Specifications
Central

## Slide 9
Conclusion
Results
Measurements
Software
Hardware
Schema Block
Notes: nRF52840, more features to not be restricted
Power Profiler Kit, performant and easily use
Accelerometer A/D Converter, quickly implemented, use serial communication
Interrupt generator, stress and measure the interrupt latency

## Slide 10
Conclusion
Results
Measurements
Software
SoftDevice S140, nRF5 SDK v13.0.0
Zephyr SDK v0.9.1, source code frequently updated from GitHub repository
Architecture

## Slide 11
Conclusion
Results
Measurements
Software
3 applications
  Peripheral connected to 1 central nRF-Connect
  Central connected to 1-8 E-Peripherals
  E-Peripheral Emulated peripherals, nRF52832 S132
2 services
Soft Timer
External interrupt
Buttons & Leds
Applications
Notes: E-Peripheral nRF52832, because possibility to have more

## Slide 12
Power Consumption
Interrupt Latency
Bluetooth Low Energy Behaviour
  Advertising interval Peripheral → defined by Bluetooth Core 4.0
  Stack Propagation Delay Peripheral
  Scanning Interval/Window Central → defined by Bluetooth Core 4.0
  Connection Interval Central → defined by Bluetooth Core 4.0
  Connection Event Interval Central
Difficult because no access to the source code of SoftDevice
Conclusion
Results
Measurements
Type
GPIOs & Logic Analyser
PPK
Notes: Interval, define by Bluetooth core, work or not

## Slide 13
Conclusion
Results
Measurements
Interrupt Latency

## Slide 14
Conclusion
Results
Measurements
BLE Interval

## Slide 15
Conclusion
Results
Measurements
BLE Interval

## Slide 16
Conclusion
Results
Measurements
BLE Stack Propagation Delay

## Slide 17
Conclusion
Results
Measurements
Example of measurement

## Slide 18
Conclusion
Results
Measurements
Use cases
Based on examples of nRF5 SDK v13.0.0
Central tested with 1, 4, 8 peripherals connected
Notes: - Examples from nRF5 SDK
Case 1, worst cases, central only one connection.
Case 2, save power, good throughput,
Case 3, power more important

## Slide 19
Conclusion
Results
Measurements
Test cases
Notes: Interrupt increase until break

## Slide 20
Conclusion
Results
Power Consumption without BLE
Chart: Compare Power Consumption, INterrupT AND Drivers
| 0 | 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Zephyr, TIMER OFF, ACC /ADC OFF | 600 | 637 | 1330 | 2050 | 2970 | 3820 | 3510 | 4150 | 3510 | 4170 | 4260 | 5080
SD+SDK, TIMER OFF, ACC /ADC OFF | 195 | 0 | 1440 | 2320 | 3580 | 4740 | 3980 | 4040 | 4200 | 4740 | 5140 | 4930
Zephyr, TIMER ON, ACC /ADC ON | 1010 | 1110 | 1550 | 2400 | 3260 | 4070 | 3870 | 4470 | 4610 | 4140 | 5110 | 5510
SD+SDK, TIMER ON, ACC /ADC ON | 1120 | 1280 | 1890 | 2800 | 3790 | 4760 | 4320 | 4880 | 4960 | 4840 | 5260 | 5390
Notes: - Darker Zephyr
- Lighter SDK+SD
- Wrong sleep first measurements

## Slide 21
Conclusion
Results
Power Consumption with BLE
Chart: Peripheral Power Consumption when connected
| 0 | 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Zephyr Conn. Interval 7.5ms | 4070 | 4110 | 4520 | 5050 | 5570 | 6140 | 6070 | 6490 | 6720 | 6440 | 7030 | 7330
SD+SDK Conn. Interval 7.5ms | 4700 | 4810 | 5300 | 5870 | 6500 | 7140 | 6940 | 7340 | 7450 | 7350 | 7590 | 7620
Zephyr Conn. Interval 50ms | 2440 | 2530 | 2880 | 3500 | 4190 | 4900 | 4750 | 5280 | 5530 | 5050 | 5870 | 6250
SD+SDK Conn. Interval 50ms | 2530 | 2860 | 3290 | 3970 | 4780 | 5650 | 5270 | 5800 | 5980 | 5780 | 6100 | 6070
Zephyr Conn. Interval 400ms | 1450 | 1540 | 1940 | 2660 | 3530 | 4260 | 4050 | 4610 | 4860 | 4340 | 5240 | 5630
SD+SDK Conn. Interval 400ms | 1700 | 1790 | 2130 | 2980 | 3940 | 4950 | 4450 | 5020 | 5170 | 4990 | 5410 | 5400
Chart: Central Power Consumption when connected to 1 Peripheral
| 0 | 1 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Zephyr Conn. Interval 7.5ms | 4900 | 4940 | 5470 | 6200 | 7080 | 7970 | 7680 | 8250 | 8060 | 8270 | 8540 | 8860
SD+SDK Conn. Interval 7.5ms | 5530 | 5620 | 6050 | 6650 | 7310 | 7990 | 7680 | 7960 | 8050 | 8220 | 8450 | 8450
Zephyr Conn. Interval 50ms | 2600 | 2670 | 3030 | 3540 | 4210 | 4910 | 4650 | 5170 | 4860 | 5260 | 5310
SD+SDK Conn. Interval 50ms | 2610 | 2690 | 3170 | 3770 | 4720 | 5660 | 5120 | 5160 | 5400 | 5740 | 6070 | 5860
Zephyr Conn. Interval 400ms | 1400 | 1400 | 1870 | 2450 | 3270 | 4110 | 3780 | 4350 | 4510 | 4540 | 4520 | 5240
SD+SDK Conn. Interval 400ms | 926 | 1030 | 1760 | 2550 | 3750 | 4850 | 4180 | 4110 | 4430 | 4880 | 5280 | 4910

## Slide 22
Conclusion
Results
Interrupt Latency
Chart: Interrupt Latency of the extension board
| Interrupt | Interrupt and Soft-Timer | Interrupt, Soft-Timer and Drivers
Zephyr avg. | 7.0772 | 14.9673 | 14.8681
SD+SDK avg. | 6.5962 | 6.834 | 6.4533
Zephyr min | 6.7708 | 7.0798 | 7.4366
SD+SDK min | 6.5417 | 6.4163 | 6.2913
Zephyr max | 10.6667 | 16.584 | 24.542
SD+SDK max | 6.7292 | 10.563 | 13.6243
Chart: Interrupt Latency of the peripheral
| Advertising | Conn. Interval 7.5ms | Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 14.6233 | 14.4664 | 14.8757 | 14.8684
SD+SDK avg. | 6.4159 | 7.938 | 6.747 | 6.5333
Zephyr min | 10.6 | 6.6017 | 10.5617 | 7.2458
SD+SDK min | 6.2292 | 6.2708 | 6.2933 | 6.24
Zephyr max | 17.68 | 26.6475 | 20.9375 | 24.8335
SD+SDK max | 9.8542 | 39.9165 | 12.2667 | 17.74
Chart: Interrupt Latency
| Advertising | Conn. Interval 7.5ms | Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 14.6233 | 14.4664 | 14.8757 | 14.8684
SD+SDK avg. | 6.4159 | 7.938 | 6.747 | 6.5333
Zephyr min | 10.6 | 6.6017 | 10.5617 | 7.2458
SD+SDK min | 6.2292 | 6.2708 | 6.2933 | 6.24
Zephyr max | 17.68 | 26.6475 | 20.9375 | 24.8335
SD+SDK max | 9.8542 | 39.9165 | 12.2667 | 17.74

## Slide 23
Conclusion
Results
Stack Propagation Delay
Chart: Stack Propagation delay
| Conn. Interval 7.5ms | Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 95.5 | 91.6925 | 93
SD+SDK avg. | 56.9851 | 45.4052 | 45.6
Zephyr min | 81.7 | 81.6875 | 82
SD+SDK min | 43.125 | 35.2 | 32
Zephyr max | 256 | 222.188 | 170
SD+SDK max | 241.875 | 53.76 | 154

## Slide 24
Conclusion
Results
Connection Event Interval
Chart: Connection events Interval, 1 Peripherals
| Conn. Interval 7.5ms | Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 5.971 | 9.2544 | 21.4574
SD+SDK avg. | 1.7401 | 2.0808 | 2.0802
Zephyr min | 5.8886 | 0.95656 | 18.1215
SD+SDK min | 0.9728 | 1.9681 | 2.0699
Zephyr max | 6.0458 | 37.5102 | 24.7618
SD+SDK max | 2.0869 | 2.1029 | 2.0869
Chart: Connection events Interval, 4 Peripherals
| Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 21.5094 | 34.3364
SD+SDK avg. | 13.3368 | 13.3296
Zephyr min | 15.2653 | 31.3099
SD+SDK min | 13.3204 | 13.3205
Zephyr max | 28.4977 | 38.4825
SD+SDK max | 13.3537 | 13.3374
Chart: Connection events Interval, 8 Peripherals
| Conn. Interval 50ms | Conn. Interval 400ms
Zephyr avg. | 30.109 | 44.3027
SD+SDK avg. | 28.3347 | 28.3316
Zephyr min | 23.5338 | 40.7067
SD+SDK min | 28.3203 | 28.3193
Zephyr max | 37.3952 | 47.2987
SD+SDK max | 28.3538 | 28.3513

## Slide 25
Conclusion
Results
Connection Event Interval
SoftDevice
Zephyr

## Slide 26
Conclusion
Results
Summary
Power Consumption
  Zephyr slightly lower than SD+SDK
Interrupt Latency
  Zephyr: 15µs SD+SDK: 7µs
Break Frequency
  Zephyr: 130kHz SD+SDK: 130kHz
Bluetooth Low Energy Behaviour
  Advertising interval OK
  Scanning Interval/Window OK
  Connection Interval OK
Notes: Break frequency, higher, not important in this case because interrupt latency

## Slide 27
Conclusion
Zephyr RTOS performance
  Satisfy the conditions
  Near SD+SDK
My impression
  Better API Documentation
  Easier to configure
Questions ?
Conclusion